## Slide 1: Generation of Ultrahigh Peak Power Pulses by Chirped Pulse Amplification
P. Maine, D. Strickland, P. Bado, M. Pessot, G. Mourou (IEEE J. Quantum Electronics, 1988)

## Slide 2: Core Idea
A short laser pulse is first stretched (chirped) to reduce peak power, amplified safely, and then compressed again.
• Overcomes nonlinear effects in amplifiers.
• Achieves peak power up to 0.5 TW.
• Forms the basis for petawatt-class lasers.

## Slide 3: Limits of Short-Pulse Amplification
1. The amplifier bandwidth must support the full pulse spectrum.
2. Fluence should be near the saturation fluence: Fs = hν / σ.
3. Intensity must stay below the nonlinear limit (B-integral):
B = (2π / λ) ∫ n₂ I(z) dz ≤ 5.

## Slide 4: Principle of Chirped Pulse Amplification (CPA)
1. Pulse stretcher – expands the pulse in time.
2. Amplifier – increases energy at low peak intensity.
3. Compressor – restores the short duration.
↓
Produces a short, high-energy pulse.
[Insert Figure 1 – CPA setup diagram]

## Slide 5: Experimental Setup
• Laser: CW mode-locked Nd:YLF, λ = 1.053 µm, 55 ps pulses.
• Stretching: 1.3 km single-mode fiber → 300 ps.
• Amplification: Nd:glass → up to 1 J energy.
• Compression: 1700 lines/mm gratings → 1 ps.
• Peak power: 0.5 TW.
[Insert Figure 2 or Figure 4 – experimental layout.]

## Slide 6: Key Equations
Saturation fluence: Fs = hν / σ.
Nonlinear phase shift (B-integral): B = (2π / λ) ∫ n₂ I(z) dz.
Group delay from grating pair:
τ(λ) = τ₀ + τ₁ + τ₂ = Lλ / (c a cos²θ) + 3Lλ² / (c a² cos³θ).

## Slide 7: Experimental Results
• Pulse energy: 0.5 J.
• Duration: 1 ps.
• Peak power: 0.5 TW.
• Beam divergence: 2.2× diffraction limit.
• Brightness: ~10²¹ W/(cm²·sr).
[Insert Figure 6 – autocorrelation trace.]

## Slide 8: Toward Petawatt Power
If stretched to 1 ns and amplified to 1 kJ:
P = E / τ = 1 kJ / 1 ps = 1 PW.
• Enables intensities above 10²³ W/cm².
[Insert Figure 11 – expansion–compression setup.]

## Slide 9: Conclusions
• CPA allows short-pulse amplification without nonlinear distortion.
• Achieved 0.5 TW peak power in a compact tabletop system.
• Opened the path to petawatt lasers and modern ultrafast optics.